## Slide 1
Networks and Security
How Networks Work
Notes: <number>

## Slide 2: Introduction
- Network communication is accomplished by passing data through a logical framework of layered protocols
Objectives
- Describe the responsibilities, protocols, and hardware associated with network layers
- Describe how to secure network layers
Notes: <number>

## Slide 3: Circuit vs. Packet Switching
POTS vs VOIP
Internet Backbone maps at http://www.nthelp.com/maps.htm
Notes: <number>

## Slide 4: Network Layers
The International Standards Organization has developed the Open Systems Interface (OSI) Model – the defacto standard for defining network layers.
- Segmenting network operation into layers promotes flexible and interoperable network systems
Each layer has a set of operations it performs on network data – receiving dta from an adjacent layer and forwarding it on to the other adjacent layer.
- Network devices don’t have to use every layer in the OSI model; but if they want to communicate the layers (and associated protocols) they use must match.
Notes: <number>

## Slide 5: Layer 1: Physical Layer
-The Physical Layer is responsible for transmitting bits across a network
-Physical Layer protocols define…
- Media (UTP, coax, fiber-optic, wireless),
- Cable Connectors (RJ-45, F-Connector, SC),
- Signal Encoding (electrical, optical, RF),
- Transmission Speed (10, 100, 1000, or 11 Mb/sec),
- Transmission Distance (100m., 5Km., 70’)
Notes: <number>

## Slide 6: Layer 1: Physical Layer
Example Physical Layer Components…
Ethernet WiFi
802.3 802.11b
Media UTP/Cat3 2.4 GHz
Connector RJ-45 --------
Encoding Manchester DSSS
Speed 10 Mb/sec 11 Mb/sec
Distance 100 meters 70’
Notes: <number>

## Slide 7: Layer 1: Physical Layer Hardware - Hub/Repeater
Hubs amplify and retime signals – after regenerating a signal from one port the signal is forwarded out all ports.
Hubs forward traffic very quickly – add very little latency to network transmission.
-Hubs only accommodate a single data transmission at any point in time
https://www.youtube.com/watch?v=reXS_e3fTAk&feature=related
Notes: <number>

## Slide 8: Layer 2: Data Link Layer
-The Data Link Layer is responsible for forwarding chunks of data (packets) between two devices on the same network.
-Data Link Layer protocols define…
- Addressing within a network,
- The amount of data within a packet (min and max)
- Error-checking for packets
Notes: <number>

## Slide 9: Layer 2: Data Link Layer
- Data Link Layer protocols can be categorized as Local Area Networks (LANs), Wide Area Networks (WANs), or Metropolitan Area Networks (MANs) protocols
- Data Link Layer protocols include…
Ethernet Frame Relay
ATM Serial (T1, DS3, OC3)
WiFi
Token Ring
FDDI
Notes: <number>

## Slide 10: Layer 2: Data Link Layer Hardware - Switch/Bridge
-Switches amplify and retime signals; they area also capable of making intelligent forwarding decisions based on Layer 2 address information (a Media Access Control Address – MAC address Table).
-Switches read an entire packet before making a forwarding decision – slight higher latency.
-Switches will only forward well-formed packets
-Switches collect the MAC addresses of devices in a MAC Table as they transmit data. The switch will use its MAC Table to forward packets out a specific port. This process allows multiple simultaneous transmissions – improving network throughput.
-Switches will forward broadcast packets out all ports. If a packet is destined to an address that is not in the MAC Table it is forwarded out all ports.
Notes: <number>

## Slide 11: Layer 3: Network Layer
- The Network Layer is responsible for transmitting data between two devices on possibly different networks.
- Network Layer protocols define…
- Network layer addressing that can span beyond a
single network
- Network Layer protocols examples…
- IP (and IPv6)
- IPX/SPX (Novell)
- AppleTalk
Notes: <number>

## Slide 12: Layer 3: Network Layer Hardware - Router
-Routers forward traffic between possible diverse Layer 2 networks based on Layer 3 address information (a Route Table).
-Routers read an entire packet before making a forwarding decision – having to process Layer 3 information deeper in the packet. This extra processing adds more latency than switches.
-Routers will only forward well-formed packets
-Routers use a Route Table to collect network information from other networked routers (possibly spanning ISPs). The router will use its Route Table to forward packets to the next-hop router (the next router on the path to the packets final destination).
-Routers will not forward broadcast packets.
Notes: <number>

## Slide 13: Circuit vs. Packet Switching
POTS vs VOIP
Internet Backbone maps at http://www.nthelp.com/maps.htm
Notes: <number>

## Slide 14: Layers 4-7: “Application” Layers
- The “Application” Layers are responsible for transmitting data between two devices on possibly different networks – data could be in the form of email, web page, or file download.
- “Application” Layer protocols define…
- Connection-based (i.e. request retransmission to guarantee delivery) and Connectionless communication formats
- Port-based communication
- TCP and UDP are two of the most common protocols in this group
Notes: <number>

## Slide 15: Layers 4-7: “Application” Layers
TCP is connection oriented (devices must establish a connection before transmission begins and send response after receipt) making it reliable over packet-switched networks.
- UDP is connectionless (server sends packets in ‘fire and forget’ mode) making it less reliable for communication; the application itself must process any errors and check for reliable delivery
Notes: <number>

## Slide 16: Layers 4-7: “Application” Layers
A port is a number used for host-to-host communication, identifying which higher-level protocol or application (process) should receive a message. Each application has a designated (often well-known) port number
Application Layer protocols and their ports include...
- HTTP (TCP 80), FTP (TCP 20,21)
- DHCP (UDP 67/68) automatically assigns IP settings
- Telnet (TCP 23) used for remote console
connections
Notes: <number>

## Slide 17: Network Layers
Notes: <number>

## Slide 18: Network Operation
-Connect patch cable to NIC card on computer and network jack.
-The ethernet switch learns the computer’s MAC address and enters it in its MAC Table
-The computer receives an IP address (via DHCP protocol)
-The computer launches a web-browser and requests a connection to www.google.com
-The DNS protocol translates the IP Name (www.google.com) to an IP Address.
-The computer tests is www.google.com is on its LAN; if not forward packet to default gateway (via LAN switches).
-Routers between computer and google forward the packets hop-by-hop based on their route table information (crossing multiple ISPs in the process)
Notes: <number>

## Slide 19
Networks and Security
- Threats and Controls
Notes: <number>

## Slide 20: Network Security
Network security threats can come from:
-Hackers
-Malware
-Viruses
-Insider Threat
Network security threats attempt to:
-Steal or manipulate data off the network or a
networked system
-Gain control systems (install zombie processes, root-
kits, or spam relays) -Generate denial-of-service (DOS) conditions (attack
bandwidth, cpu, or memory of networked systems)
Notes: <number>

## Slide 21: Network Security – Physical Layer (Layer 1)
Physical Layer attacks rely on having access to the target’s transmission media (physical cabling, RF frequency, etc.).
Objective #1: Choose transmission media wisely.
-RF is much easier to “sniff” (capture network traffic off the media) than UTP or fiber-optic cabling
Objective #2: Avoid Hubs.
-Hubs repeat traffic out all ports – makes it easy to sniff traffic by just plugging in.
Notes: <number>

## Slide 22: Network Security – Physical Layer (Layer 1)
Objective #3: Protect access to wireless access-points
- Use lists of authorized MAC addresses to make sure only authorized devices can connect to the access point
-Use encryption keys (WEP) to protect from unauthorized eavesdropping. WPA is stronger than WEP.
Notes: <number>

## Slide 23: Network Security – Data Link Layer (Layer 2)
Data Link Layer attacks rely on having access to the target’s local network
Objective #1: Protect switch’s MAC Table
-Attackers can try to ‘poison’ the MAC Table – which can make the switch function more like a hub forwarding traffic out all ports, then sniff traffic
-Use manageable switches so that MAC addresses in MAC table can be specified and monitored
Notes: <number>

## Slide 24: Network Security – Data Link Layer (Layer 2)
Objective #2: Secure management access to network switches
- Don’t let attacker use the switch as a platform for other
attacks (secure Telnet, HTTP, and management protocols)
-For manageable switches, change default user IDs,
passwords, update patches
-Most switches have a ‘port-mirroring’ function that is
helpful for troubleshooting – also makes it easy to redirect
traffic to an attacker.
Notes: <number>

## Slide 25: Network Security – Data Link Layer (Layer 2)
Objective #3: Some enterprise-level switches support filtering traffic based on source/destination IP-address, port, or MAC address (still forward based on MAC address)

## Slide 26: Network Security – Data Link Layer (Layer 2)

## Slide 27: Network Security – Network Layer (Layer 3)
Layer 3 attacks rely can originate from anywhere – inside or outside a target’s local network.
Objective #1: Don’t let attacker use the router as a platform for other attacks (secure Telnet, HTTP, and management protocols) via strong UserID and PW management - change default userID, PWs, update patches
Objective #2: Only accept Route Table information from trusted internal routers.
Notes: <number>

## Slide 28: Network Security – Network Layer (Layer 3)
Objective #3: Filter access of outside traffic to inside resources. How? On routers, use Access Control Lists (ACLs) to check incoming traffic. Also helps prevent IP Spoofing attacks
Notes: <number>

## Slide 29: Network Security – Network Layer (Layer 3)
- Router ACLs support filtering traffic based on source/destination IP-address, source/destination ports, and sometimes MAC addresses.
- ACLs can be applied to in-bound and out-bound traffic on a specific router interface.
- ACLs typically have a default DROP ANY ANY rule at the end of its rule set
interface Ethernet0/0
ip address 10.1.1.1 255.255.255.0
ip access-group 101 in
access-list 101 remark permit telnet
access-list 101 permit tcp host 10.1.1.2 host 172.16.1.1 eq telnet

## Slide 30: Network Security – Network Layer (Layer 3)
Objective #4: Filter access of outside traffic to inside resources. How? Use dedicated Firewall routers
-Network firewalls are routers that specialize in filtering (accepting or denying) traffic into and out of networks.
-Firewalls filter traffic based on a list of rules
-Firewall rules are processed in sequential order (ordering of rules is critical to effective security).
- Firewalls have a final, default rule that drops all traffic
Rule Number | Source Address | Destination Address | Protocol | Source Port Number | Destination Port Number | Action
1 | 10.56.2.99 | * | * | * | * | Pass
2 | 10.122.* | 10.56.* | TCP | 23 (Telnet) | * | Pass
3 | 10.56.* | 10.122.* | TCP | * | 23 (Telnet) | Pass
4 | * | 10.56.2.95 | TCP | * | 25 (mail) | Pass
5 | * | * | * | * | * | Drop
Notes: <number>

## Slide 31: Network Security – Network Layer (Layer 3)

## Slide 32: Network Security – “Application” Layers (Layers 4-7)
’Application’ Layer attacks rely can originate from anywhere – inside or outside a target’s local network.
Objective #1: Use Intrusion Protection Systems to detect/block network scans, probes, and attacks
- Intrusion Prevention Systems look at patterns of network traffic from network devices (traffic could be spread across multiple packets) - Intrusion Prevention Systems can block traffic based on payload contents – acting like an ‘application layer firewall’
- e.g., if router/switch compromised might see many access attempts to application or database using default IDs/PWs. IPS would watch for this.
Notes: <number>

## Slide 33: Network Security – “Application” Layers (Layers 4-7)
Objective #2: Use Virtual Private Networks to secure communication between network devices
-Data is encrypted between network devices to prevent people from sniffing traffic
- VPNs can connect remote-clients to home networks.
- VPNs can connect two corporate networks together.
Notes: <number>